## Slide 1: Surface Telerobotics Human Exploration Telerobotics (HET) Project Technology Demonstration Mission (TDM) Program Space Technology Mission Directorate (STMD)
Terry Fong
HET Project Manager
Intelligent Robotics Group
NASA Ames Research Center
terry.fong@nasa.gov

## Slide 2: Motivation
Candidate Missions
  L2 Lunar Farside. Orion crew module test flight (~2020) to Earth-Moon L2 point
  Near-Earth Asteroid. NEA dynamics and distance make it impossible to manually control robot from Earth
  Mars Orbit. Crew must operate surface robot from orbit when circumstances (contingency, etc.) preclude Earth control
What will the test achieve?
  Obtain baseline engineering data
  Validate & correlate prior ground simulations
  Reduce the risk that mission planning is based on inaccurate assumptions
  Surface Telerobotics is an engineering test of a human-robot “opscon” for future deep-space human exploration missions
(NASA GSFC)
Notes: Human Exploration Telerobotics
Scenario: humans in orbit remotely operating robot on surface
Lots of hypotheses, many assumptions, almost NO hard data
Data is needed to design, build, and operate:
- control mode
- comm
- robot systems
- UI requirements

## Slide 3: Surface Telerobotics
Objectives
  Demo crew-centric control of surface telerobot from ISS (first operational system) based on L2 Lunar farside mission concept
  Test human-robot “opscon” for future deep-space exploration mission
  Obtain baseline engineering data of system operation
Approach
  Leverage best practices and findings from prior ground simulations
  Collect data from robot software, crew user interfaces, and ops protocols
  Validate & correlate to prior ground sim (analog missions 2007-2011)
Implementation
  K10 planetary rover in ARC Roverscape (outdoor test site)
  ISS astronaut + Mission Control
  L2 mission sims (3): June-Aug 2013 (ISS Incr. 36: 10.5 hr total crew time)
K10 at NASA Ames
Crew on ISS
Key Points
Complete human-robot mission sim: site selection, ground survey, telescope deployment, inspection
Telescope proxy: COTS 75 micron polyimide film roll (no antenna traces, no electronics, no receiver)
3.5 hr per crew session (“just in time” training, system checkout, telerobot ops, & crew debrief)
Two control modes: basic teleop and pre-planned command sequencing (with continuous monitoring)
Limited crew user interface: no sequence planning, no science ops capability, no robot engineering data

## Slide 4: Objectives
  1. Demonstrate that crew can remotely operate surface robots from inside a flight vehicle to perform exploration work
    Ability to supervise planetary robot from space craft (make correct decisions, take appropriate action)
    Awareness of intent and outcome of rover autonomous actions for waypoint driving, image acquisition, payload deployment
    Ability to detect and respond appropriately to robot problems affecting achievement of mission objectives
  2. Mature technology required for crew control of surface telerobots (specifically robotic control interfaces for crew)
    Information and capability for supervisory control of robot
    Information and capability for mission tasks of site selection, antenna deployment, and antenna inspection
    Usefulness and understandability of robot’s autonomous functions for waypoint driving, image acquisition, and payload deployment
    Availability and timeliness of information (communication & data distribution)
  3. Identify requirements and gaps for research and technology development programs
    Identify HRP risks and gaps relevant to Surface Telerobotics
    Document evidence of HRP risks or HRP risks avoided observed during sessions

## Slide 5: L2 Lunar Farside (Waypoint) Mission Concept
Orion at Earth-Moon L2 Lagrange point
  60,000 km beyond lunar farside
  Allows station keeping with minimal fuel
  Crew remotely operates robot on lunar farside
  Less expensive than human surface mission
  Does not require human-rated lander
Primary objective: lunar telescope
  Use telerobot to setup radio telescope
  Requires surface survey, antenna/receiver deployment, and inspection/documentation
  Lunar farside provides radio quiet zone for low-freq measurements cosmic dawn
Secondary objective: sample collection
  Use telerobot to perform field geology
  Requires scouting, sampling (possibly subsurface), and sample caching/return
  South Pole Aitken (SPA) basin sampling is the highest priority lunar science objective
(Lockheed Martin / LUNAR)

## Slide 6: Polyimide Antenna Technology
Concept
  Metallic conductor deposited on surface of polyimide film (e.g., DuPont Kapton)
  Suitable for frequencies up to 100 MHz
  Polyimide remains flexible at lunar daytime temperatures, thus can be deployed by unrolling
Testing (to date)
  Vacuum chamber with thermal cycling & UV exposure similar to lunar surface conditions (Univ. of Colorado Boulder / NLSI LUNAR)
  Outdoor signal test (New Mexico)
Outdoor test in New Mexico
Rolling out polyimide film inside vacuum chamber with teleoperated mini-rover
(UC-Boulder / LUNAR)
(UC-Boulder / LUNAR)

## Slide 7: Telerobotic Telescope Deployment Concept
(JPL / LUNAR)

## Slide 8: Waypoint Mission Simulation (2013)
June 17
July 10
August 8
Spring

## Slide 9: K10 Planetary Rover @ NASA Ames
NASA Ames Roverscape
K10 Specifications
4-wheel drive, 4-wheel steer
Split rocker chassis
Size: 1.3 x 0.9 x 1.0 m (HxWxL)
Speed: 0.9 m/s (on 10 deg slope)
Power: 1900 W (Li-ion batteries)
Weight: 100 kg (with 25 kg payload)

## Slide 10: Deployed Telescope Simulation
NASA Ames Roverscape

## Slide 11: Robot Interface (Task Sequence Mode)
Terrain hazards
Rover camera
display
Task
Sequence
Notes: Primary objective: maximize operator (crew) situation awareness
(this is MORE important than just a sense of “presence”)

## Slide 12: Robot Interface (Teleop Mode)
Rover path
Motion controls
Terrain hazards
Rover camera
display
Camera controls
Notes: Primary objective: maximize operator (crew) situation awareness
(this is MORE important than just a sense of “presence”)

## Slide 13: Data Communications
“Live” Rover Sensor and Instrument
Data (telemetry)
Robot User Interface on SSC
K10 rover at NASA Ames
384 kbits/sec (min), 5 sec delay (max)
Uplink
8 kbits/sec (min), 5 sec delay (max)
Downlink
384 kbits/sec (min), Out-of-Band
Uplink, data transfer
to laptop storage
Rover Task Sequence (text file)
Interface Instrumentation & Evaluation Data
Post-test File Transfer
Rover/Science Data (e.g. imagery)
Note: Normal uplink ~1Mbps, spike after LOS is ~2Mbps for 2 sec
Notes: We’re turning typical payload communications on its head
  Our payload hardware is on the ground, and the operator is on station
  Requires the use of ops LAN
    Upgrades to the payload LAN are coming

## Slide 14: Tasks & Activities (ISS Crew)
Each crew session is 3.5 hours
Review, Training, Conference (1 hour)
  Watch Intro Video, Read Big Picture Words (15 min)
  Run through Just-in-time Training module (30 min)
  Crew conference with PD team (15 min)
Surface Telerobotics Ops (2 hours)
  Downlink task plans to robot and monitor execution
    Interrupt execution for problems (e.g. cannot reach waypoint)
  Handle contingencies as needed (run “teleop” plans)
    Teleop to avoid obstacles
    Perform additional data collection as needed to reacquire data
  As observation data arrives, verify that data is valid
  Interact with ground support as needed
Debrief with mission control (0.5 hours)
Notes: The other way our payload is unique is the way we will train crew
  Intro video will give crew the context and goals of the experiment
  Self-guided GUI will train the crew member
Also unique: Debrief is part of our crew session
  Need the crew impressions of situation awareness, critical incidents, and effectiveness/ease of use of interface while it’s fresh

## Slide 15: Technology Advancement
Subsystem | Start | End
Supervisory control user interface (ST Workbench) | 5 | 6
In-line metrics, summarization, and notification systems | 4 | 6
Science data analysis interface (xGDS) | 5 | 6
Autonomy for short-delay interactive supervisory control (RoverSW) | 5 | 7
Command/telemetry messaging (RAPID) | 5 | 7
Time-delay mitigation | 4 | 7
  TRL 4 = Component and/or breadboard validation in lab
  TRL 5 = Component and/or brassboard validation in relevant environment (simulation of target operational environment)
  TRL 6 = System/subsystem model or prototype demonstration in a relevant environment (under critical conditions). Engineering feasibility fully demonstrated.
  TRL 7 = System prototype demonstration in an operational (space) environment. Well integrated with operational hardware/software.

## Slide 16: Test Protocol
Data Collection
  Obtain engineering data through automatic and manual data collection
  Data Communication: direction (up/down), message type, total volume, etc.
  Robot Telemetry: position, orientation, power, health, instrument state, etc.
  User Interfaces: mode changes, data input, access to reference data, etc.
  Robot Operations: start, end, duration of planning, monitoring, and analysis
  Crew Questionnaires: workload, situation awareness, criticial incidents
Metrics
  Use performance metrics* to analyze data and assess human-robot ops
  Human: Bedford workload rating scale & SAGAT (situation awareness)
  Robot: MTBI, MTCI for productivity and reliability
  System: Productive Time, Team Workload, and task specific measures for effectiveness and efficiency of the Human-Robot system
automatic
manual
* Performance metrics used for prior analog field tests: 2009 robotic recon, 2010 lunar suface systems, 2010 robotic follow-up, 2009-2011 Pavillion Lakes research project, etc.

## Slide 17: Schedule
  11/29/11 ISS Payloads Office authorization received
  1/30/12 ISS Research Planning Working Group approval received
  9/5/12 PCM (PLUTOs, Flight Director, MSFC, Ames)
  11/13/12 SSC Lab testing
  11/26/12 JSL Lab Testing for first Comm Test
  11/29/12 SSTF-based end-to-end test
  1/28/13 First ISS-to-ground Comm Test
  3/13 – 5/13 Engineering and Ops Readiness Tests at Ames
  4/3/13 Crew Usability Test – SSTF to Rover at Ames
  5/8/13 JSL Lab Testing for Crew Ops
  6/10/13 Second ISS-to-ground Comm Test (due to ODAR, etc.)
  6/17/13 Crew Ops session #1 – Site survey
  7/22/13 (tbc) Crew Ops session #2 – Antenna deploy
  8/5/13 (tbc) Crew Ops session #3 - Inspection
Notes: Currently developing the polyimide film deployer
  Ground demo means there will be no crew control
ISS-to-Ground comm test requires no crew time
  only crew involvement is flight note saying “Don’t touch the laptop”
Crew sessions are not yet scheduled
  Constraint of needing dry weather and daylight in Mountain View, CA
  Just possible to fit a session in at the end of the crew day that corresponds to the crack of dawn at Ames
Collaborations:
  Dan Duncavage has been instrumental in developing and getting approval for our comm path
  Crew office has given us invaluable feedback on usability and training issues
  LUNAR team is working with us on the science scenario (telescope deployment, ground science team)
  Lock-mart is helping us with the mission concept
  ESA collaboration is currently stalled pending an interagency agreement